## Slide 1: Earth Observation Tool

## Slide 2: OBJECTIVES
Define POI
By lat/long coordinates
By area
Define Constellation
Define orbit properties (altitude, satellite per plane, inclination)
Define Payload properties (swath, depointing angle, SAR, EO, data size)
Calculate KPI
Number of revisit per day (with/without depointing)
Coverage (time interval, with/without depointing)
Define Ground Segment
GS location (lat/long coordinates)
GS properties (elevation, orbital arc, data, bandwidth)
Acquisition/emptying opportunities
Define Mission
Mission parameters (time of the mission, sun zenith angle, depointing)

## Slide 3: IHM
  Main page with 3 config tabs and 1 for the result:
  - 1 tab to configure the point of interest
  - 1 tab to configure the ground segment
  - 1 tab to configure the constellation
  - 1 tab for the KPI
  Also, on this page, a map of the world will be show to see ground track, ground station location and POI location (except for the KPI’s tab)
  1 sub page to see the constellation, ground station and POI in 3D ?
  1 sub tab to choose which data to export

## Slide 4: IHM – Ground station tab
ff
Ground station
Point of interest
Constellation
Results
Name :
Elevation :
Data volume :
Bandwidth :
Location
Latitude: Longitude:
Altitude:
Add
Remove
Modify

## Slide 5: IHM – Point of interest tab
ff
Ground station
Point of interest
Constellation
Results
Name :
Type : point or area
Location
Latitude: Longitude:
Add
Remove
Modify

## Slide 6: IHM – Constellation tab
f
Ground station
Point of interest
Constellation
Results
Name :
Orbit
Semi-major axis:
Eccentricity:
Inclination:
RAAN:
Argument of perigee:
(Mean anomaly):
Number of plan:
RAAN offset:
Number of satellite:
Mean anomaly offset:
Sensor
Swath:
Depointing:
SAR or EO
Data volume:
Add
Remove
Modify
Swath
Swath+depointing

## Slide 7: Define POI
Create Point of interest
Longitude
Latitude
1
Create Area of interest
Longitude x2
Latitude x2
1
OR
Resolution step

## Slide 8: Define GROUND SEGMENT
Create Ground Station Location
Longitude
Latitude
1
2
Ground Station characteristics
elevation
Orbital arc
data
bandwidth
3
Associate GS characteristics to GS location
Option: Import pre-existing data

## Slide 9: CONSTELLATION DEFINITION
Create orbit
1
Number of plane
Altitude
Sat per plane
Inclination
Add orbit definition
Create Payload
2
Swath
Depointing angle
SAR
EO
Add Payload definition
Data size
Associate Payload to Satellite
3

## Slide 10: Define Mission
Define Mission requirements
Date and time
Sun zenith angle
1
Depointing (yes or no)
SAR with EO
2
Associate POI to Mission
3
Associate GS to Mission
2
Associate Constellation to Mission
Time step

## Slide 11: Define KPI-1
Example of KPIs format that can be interesting

## Slide 12: Define KPI-2
Example of KPIs format that can be interesting

## Slide 13: Format of exported data
Which ones ?
Acquisition/emptying windows/opportunities
Revisit per day/in day
GS opportunities
Date and time of flight over target
Format : CSV, JSON, XML

## Slide 14: Depointing strategy
Lorem Ipsum

## Slide 15: User stories
Mandatory user stories:
- As a user, I want to obtain detailed information on satellite passes over specific geographical areas to plan observations or operations.
- As a user, I want to be able to adjust the time interval and resolution step for orbit propagation calculations to strike a balance between accuracy and performance.
- As a user, I want to obtain simulation reports containing information on orbital parameters, eclipse periods and transits over geographical areas.
- As a user, I want to be able to simulate satellite constellations to model satellite networks for specific applications.
- As a user, I want to be able to integrate data from real satellites (telemetry, TLE) to compare simulations with real trajectories.
- As a user, I want to be able to export simulation data and visualizations for use in reports or other analyses.
- As a user, I want to visualize satellite coverage areas to plan communication or Earth observation missions.
Optional user stories:
- As a user, I want to be able to change the map projections for the ground track to better visualize satellite trajectories in different parts of the world.
- As a user, I want to simulate the effects of external disturbances (such as atmospheric drag and the gravitational effects of other bodies) to model more realistic orbits. - As a user, I want to visualize the eclipse periods of satellites so that I know when they are not visible from Earth.
- As a user, I want to be able to customize the user interface to display the information and visualizations most relevant to my mission.
- As a user, I want to be able to share simulations and visualizations with other users or customers for collaboration and presentation.

## Slide 16: Architecture

## Slide 17: Arbre des conséquences
Lorem Ipsum

## Slide 18: Data flow
Lorem Ipsum

## Slide 19: Class diagram
Lorem Ipsum